## Slide 1: CS315 Project Proposal: libpmp
Notes: 1. introduction: advantages, structure, how work (hit case)
2. 2 ways

## Slide 2: Outline
Problem Statement
Related Work
Proposed New Solutions
Evaluation Plan
Future Research Plan
Current work and difficulty
Notes: 1. introduction: advantages, structure, how work (hit case)
2. 2 ways

## Slide 3: Problem Statement
Notes: 1. introduction: advantages, structure, how work (hit case)
2. 2 ways

## Slide 4: Memory Protection
Provide a mechanism to manage the privilege of memory access.
In Linux, mprotect is used to set access privilege of different memory segments.
Usually implemented by set the bits in PTE (low efficiency).
Notes: 1. introduction: advantages, structure, how work (hit case)
2. 2 ways

## Slide 5: Intel MPK
Group several pages into a page group.
Use 16 memory protection keys (stored in a thread level PKRU register) to encode the privilege of one page group
Notes: 1. introduction: advantages, structure, how work (hit case)
2. 2 ways

## Slide 6: Hidden issues in MPK
Protection-key-use-after-free
Protection key limitation
Inter-thread synchronization for multi-thread programs
Those issues have been fixed by libmpk.
Notes: 1. introduction: advantages, structure, how work (hit case)
2. 2 ways

## Slide 7: RISC-V Physical Memory Protection (PMP)
Provide a per-hart level physical memory access privilege.
Use 16 PMP entries instead of protection key.
PMP entries consist of configuration registers and address registers
  Configuration register: use several bits to encode privilege
  Address register: Specify the managed memory region
Notes: 1. introduction: advantages, structure, how work (hit case)
2. 2 ways

## Slide 8: RISC-V Physical Memory Protection (PMP)
Notes: 1. introduction: advantages, structure, how work (hit case)
2. 2 ways

## Slide 9: Whether those three issues exist in PMP?
Protection-key-use-after-free TO BE CONTINUED
Protection key limitation EXISTS
Inter-thread synchronization EXISTS
Notes: 1. introduction: advantages, structure, how work (hit case)
2. 2 ways

## Slide 10: Protection-key-use-after-free in PMP
Protection-key-use-after-free TO BE CONTINUED
  RISC-V PMP uses PMP entries instead of protection key.
  No specification on the free for PMP entries, need experiments.
Notes: 1. introduction: advantages, structure, how work (hit case)
2. 2 ways

## Slide 11: Protection key limitation in PMP
Protection key limitation EXISTS
  Each hart only has 16 PMP entries.
  If a hart request for 17 memory isolation request, one of the PMP entries will be overwritten.
Notes: 1. introduction: advantages, structure, how work (hit case)
2. 2 ways

## Slide 12: Hidden Issues in RISC-V PMP
Inter-thread synchronization EXISTS
  Each hart has its own 16 PMP entries.
  One thread on a hart edits PMP entries, the other thread on another hart cannot be synchronized.
Notes: 1. introduction: advantages, structure, how work (hit case)
2. 2 ways

## Slide 13: Why it is Important?
Protection key limitation
  If one program issue 17 memory isolation request, current design cannot support it.
Inter-thread synchronization
  Inconsistent behavior between threads in a process: one thread set memory region M to be not readable, if not synced, other thread can read M.
Notes: 1. introduction: advantages, structure, how work (hit case)
2. 2 ways

## Slide 14: Related Work
Notes: 1. introduction: advantages, structure, how work (hit case)
2. 2 ways

## Slide 15: Protection Key Virtualization
Create more than 16 page groups
a cache-like structure
2 ways for mapping:
  thread-local
    mpk_begin() & mpk_end() by a calling thread
    sleep when fail
    page not be used -> evict and disable permission
  global
    mpk_mprotect() for all threads
    LRU for replacement
    reserves one key for execute-only pages
      merge execute-only pages group
      evicted when execute-only pages
Notes: 1. introduction: advantages, structure, how work (hit case)
2. 2 ways

## Slide 16: Inter-thread Key Synchronization in MPK
One thread calls mpk_mprotect()
mpk_mprotect() calls do_pkey_sync(pkey)
do_pkey_sync(key) sends interrupt to other threads
When other threads are scheduled, update PKRU by calling registered callback functions (callback functions are added by task_work_add())
Notes: 1. introduction: advantages, structure, how work (hit case)
2. 2 ways

## Slide 17: Source Code for Inter-thread sync
In /libmpk/kernel/mm/mprotect.c/do_pkey_sync(val_pkru)
Notes: 1. introduction: advantages, structure, how work (hit case)
2. 2 ways

## Slide 18: Propose New Solutions
Notes: 1. introduction: advantages, structure, how work (hit case)
2. 2 ways

## Slide 19: New Solution to Protection Key Limitation
Protection key limitation
  Virtual key -> Hardware key -> Page group
  Cache-like structure is used to map the virtual key to hardware key
  The frequently updated virtual key will mapped to the hardare key, the limitation is hidden by the virtual key
Inter-thread synchronization
  calling thread --interrupt (callback is to change the PKRU value) -> other threads
  other threads are scheduled -> respond to the interrupt
  -> synchronize PKRU
Notes: 1. introduction: advantages, structure, how work (hit case)
2. 2 ways

## Slide 20: New Solution to Inter-thread Sync
Current Solution: Similar to MPK
  Send interrupt to other threads.
  Register callback function to sync PMP entries.
Notes: 1. introduction: advantages, structure, how work (hit case)
2. 2 ways

## Slide 21: Evaluation Plan
Notes: 1. introduction: advantages, structure, how work (hit case)
2. 2 ways

## Slide 22: Evaluation Plan
Similar to the evaluation plan of libmpk
Several aspects:
  Security Evaluation
  Microbenchmark
  Macrobenchmark

## Slide 23: Security Evaluation
PMP: prevent the malicious code from executing privileged instructions
libpmp should implement the basic function of protecting the memory space

## Slide 24: Microbenchmark
Cache performance
  Determined by cache hit/eviction rate
Memory overhead
  Decided by memory space and internal data structure
Synchronization
  Affected by context switch
  Compared with original PMP implementation

## Slide 25: Macrobenchmark
Measure performance in several applications like libmpk
libmpk application benchmarks:
  OpenSSL
  JavaScript JIT Compilers
  In-Memory Key-Value Store

## Slide 26: Future Research Plan
Notes: 1. introduction: advantages, structure, how work (hit case)
2. 2 ways

## Slide 27: Future Research Plan
Make a survey on RISC-V TEE: Keystone/Penglai
Explore the hardware extensions to support Unlimited PMP Entries
Investigate other virtualization techniques.
Notes: 1. introduction: advantages, structure, how work (hit case)
2. 2 ways

## Slide 28: Current Work and Difficulty
Notes: 1. introduction: advantages, structure, how work (hit case)
2. 2 ways

## Slide 29: Current Work
We have prepared a docker image with RV64 architecture.
Notes: 1. introduction: advantages, structure, how work (hit case)
2. 2 ways

## Slide 30: Current Difficulty
Cannot get the value of PMP CSRs on riscv-linux-gnu gdb.
However, on the riscv-linux-gnu gdb manual:
Notes: 1. introduction: advantages, structure, how work (hit case)
2. 2 ways